## Slide 1: Zurich HDAWG GUI (AWG_gUI.py)
Richard McManus
March 2023

## Slide 2: Control Panel
Browse for waveform folder
Load waveforms from .csv file
Specify:
  primary and secondary devices
  sample rate and frequency of waveforms
  duration of playback
  triggers
    sync trigger between devices
    enable trigger to initiate playback

## Slide 3: Sequences Tab
Displays primary and secondary sequences
  Generated from control panel configuration
  Uploaded to HDAWGs via Zurich’s Python LabOne API

## Slide 4: Settings Tab
Configures delay compensation
  Sample Clock Offset rotates secondary device wave array
    Sample Rate Dependent
    Discrete values of 1/(sample rate)
      0.4167 ns for 2.4 Gsps
  Sequence Clock Offset delays primary device sequence
    Discrete values of 3.33 ns
  Total = Sequence - Sample

## Slide 5: Common Configuration
Reference Clock
Sync Trigger
Front Panel
  Sync Trigger
    HDAWG 1, Mark 1 to HDAWG 2, Trig 1
Back Panel
  Reference Clock
    HDAWG 2, Reference Clk Out to HDAWG 1, Reference Clk In
Primary
Secondary