## Slide 1: Zurich HDAWG Python Gui • PCB Layout with Eagle
Richard McManus
Research Presentation (II Credits)
Snider Group
Fall 2023

## Slide 2: Zurich HDAWG GUI (AWG_gUI.py)

## Slide 3: Background
MIPS
FPGA
PC
AWG
Power Supply
FPGA program bit-stream download (JTAG)
FPGA upload program results after program is completed (JTAG)
-IO 16 Bit (In/Out)
-Mem/Write (Out)
-PC Out 16 Bit
-Reset 1 Bit In
AWG Trigger 1 Bit
12 Positive Ramps
Power Supply
Level Shifting
Clocking Board
24 +/- Ramps
0 - 1.8v <-> +/-0.7V
0-1.8v <-> 0 – 1.2 V

## Slide 4: Spring 2021
Jack Bannon
LabOne Interface
Hardcoded values
Cut and joined ramp and rectangular waves

## Slide 5: Fall 2021
Collaboration with Jack Bannon
ReadandCreateWave(1.2).py
LabOne Python API
Ran from the command line
Loaded file from the command line
Still hardcoded (except waveform file)
Could not specify frequency
Devices not synchronized (limited to 8 channels)

## Slide 6: Spring 2023
AWG_GUI.py
(Overview)

## Slide 7: Control Panel
Browse for waveform folder
Load waveforms from .csv file
Specify:
  primary and secondary devices
  sample rate and frequency of waveforms
  duration of playback (wavelengths)
  triggers
    sync trigger between devices
    enable trigger to initiate playback

## Slide 8: Sequences Tab
Displays primary and secondary sequences
  Generated from control panel configuration
  Uploaded to HDAWGs via Zurich’s Python LabOne API

## Slide 9: Settings Tab (Used to Sync Devices)
  Sample Clock Offset (Fine)
    rotates secondary device wave array
    Sample Rate Dependent
    Discrete values of 1/(sample rate)
      0.4167 ns for 2.4 Gsps
  Sequence Clock Offset (Coarse)
    delays primary device sequence
    Discrete values of 3.33 ns
  Total = Sequence - Sample

## Slide 10: Common Configuration
Reference Clock
Sync Trigger
Front Panel
  Sync Trigger
    HDAWG 1, Mark 1 to HDAWG 2, Trig 1
Back Panel
  Reference Clock
    HDAWG 2, Reference Clk Out to HDAWG 1, Reference Clk In
Primary
Secondary

## Slide 11: Under the hood

## Slide 12: Specifying Frequency
def create_interp_array(filename, frequency, sampleRate):
# Function that loads a csv file and interpolates sample points to achieve desired frequency from specified sample rate
array = np.loadtxt(filename, delimiter=",") # Load csv file into array
numCols = len(array[0])
magnitude = [] # Initialize list for y coordinates
for i in range(numCols): # Interpolate each column/waveform
time = np.linspace(0, len(array[:,i]), int(sampleRate/frequency), endpoint = True)
magnitude.append(np.interp(time,np.linspace(0,len(array[:,i]),len(array[:,i]), endpoint = False),array[:,i]))
magnitude = np.transpose(magnitude)
return magnitude # Return interpolated 2D array

## Slide 13: Syncing Devices – Reference Clock
Reference Clock
Primary
Primary
Secondary
Secondary
PC
runtime
runtime = 0
program
program
wait for trigger
Programming disrupts reference clock
Uses internal clock of secondary device
  Programmed First

## Slide 14
Syncing Devices – Offsets
No Offset
Sequence Clock Offset
Sample Clock Offset
Primary
Secondary

## Slide 15: Comparison of Zurich Hdawg Synchronization Methods

## Slide 16: Method 1: Zurich PQSC

## Slide 17: Zurich Example PQSC Synchronization (Synchronization of multiple HDAWGs)
AWG Sequencer
PQSC Output

## Slide 18: Zurich Example PQSC Synchronization Recreated
20ns per division
200ps per division
Delay of ~250ps

## Slide 19: Zurich PQSC Ramp Wave Test (75 Mhz), Wave 8 of 12, Two HDawgs
2ns per division
200ps per division
Delay of ~250ps

## Slide 20: Method 2: Delay Compensation (AWG_GUI.py)

## Slide 21: Delay Compensation Ramp Wave test (75 Mhz), Wave 8 of 12, TWO HDAWGS
2ns per division
200ps per division
Delay of ~150ps

## Slide 22: Delay Compensation Ramp Wave test (37.5 Mhz), Wave 8 of 12, TWO HDAWGS
Scope Ch. | HDAWG # | HDAWG CH.
1 | 1 | 1
2 | 1 | 2
3 | 2 | 1
4 | 2 | 2
2ns per division
200ps per division
Delay between HDAWGs (Scope Ch. 2 and Ch. 3): 100ps – 150ps
Delay between channels of HDAWG #1 (Scope Ch. 1 and Ch. 2): 200ps – 250ps
Delay between channels of HDAWG #2 (Scope Ch. 3 and Ch. 4): 150ps – 200ps

## Slide 23: Comparison of Methods
Method 1: Zurich PQSC
Delay of ~250ps
Equal to or greater than the delay between subsequent channels of the same HDAWG
Method 2: Delay Compensation
Delay of ~150ps
Equal to or less than the delay between subsequent channels of the same HDAWG

## Slide 24: PCB Layout with Eagle

## Slide 25: Background
MIPS
FPGA
PC
AWG
Power Supply
FPGA program bit-stream download (JTAG)
FPGA upload program results after program is completed (JTAG)
-IO 16 Bit (In/Out)
-Mem/Write (Out)
-PC Out 16 Bit
-Reset 1 Bit In
AWG Trigger 1 Bit
12 Positive Ramps
Power Supply
Level Shifting
0 - 1.8v <-> +/-0.7V
0-1.8v <-> 0 – 1.2 V
Clocking Board
24 +/- Ramps

## Slide 26: Board #1 F2Ce

## Slide 27: Fall 2022
F2CE_V2
58 voltage divider modules for level shifting in and in/out signals
26 out signals do not require level shifting

## Slide 28: Spring 2023
Design changed to incorporate a main board and daughter board
88 Pin Header Interface

## Slide 29: F2CE_V3.0
Utilized resistor arrays
  60 ohm 4 resistors array
  120 ohm 8 resistors array

## Slide 30: F2CE_V3.1
Implemented Power Regulator
  ADP171
Set resistor values to provide 1.2 V
  R1 = 510 ohm
  R2 = 360 ohm
Board was ordered from Elecrow

## Slide 31: F2CE_V3.1 Assembly
Assembled with Ricky

## Slide 32: F2CE_V4
Discovered bi-directional IO requires input and output pins

## Slide 33: F2CE_V4.0
Implemented bi-directional redesign
  15 additional traces routed
Board was ordered from Elecrow

## Slide 34: Board #2 F2CE Daughter Board

## Slide 35: F2CE_Daughter
AnnahMarie laid out board
Compressed board
Centered Connectors
Ordered board from Elecrow

## Slide 36: Board #3 Active Level Shifting Board

## Slide 37: Circuit (Designed by Dr. Orlov)
Active Level Shifting
FPGA: 0 – 1.8V
MIPS: +/- 0.7 V
Utilizes 2 Comparators per bit
Direction-Controlling MOSFET

## Slide 38: First Attempt

## Slide 39: LLS_V3_8x2_Inline
Discovered Design Blocks
  Can copy and paste a pre-laid out circuit
  Caveat: cannot change design block after implementation
Dr. Orlov laid out board
Helped with warnings and errors
Organized silkscreen
Compressed board
Ordered board from Elecrow

## Slide 40: Communication and Collaboration

## Slide 41: LLS_V3_8x2_Inline Assembly
Assembled 1 channel with Ricky

## Slide 42: LLS_V4_8x2_Inline
Dr. Orlov implemented 2 – pin bi-directional design
Helped with warnings and errors
Ordered board from Elecrow

## Slide 43: Next Steps
Assemble Boards (In EIH)
Test functionality